## Slide 1
SR source related calculations with SRW
Luca Rebuffi
lrebuffi@anl.gov
Optics Group, Advanced Photon Source
Rafael Celestre
rafael.celestre@gmail.com
Groupe Optique, Division Expériences, Synchrotron SOLEIL

## Slide 2: SR source related calculations with SRW
Outline:
What do we want from source related calculations?
Which elements constitute the source in SRW?
How is it done?
Live demo using OASYS

## Slide 3: What do we want from source related calculations?
Spectral properties:
“on axis” or “through slit” photon flux (and tuning curves for undulators);
spectral brightness;
coherent flux and fraction;
spectral & cumulated power (“total” or “through slit”)…
Spatial properties:
beam profile or angular distribution (intensity and phase);
coherent mode decomposition, cross spectral density, mutual intensity…
power density…
Spectral distribution of spatial properties and spatial distribution of spectral properties (3D data sets)…

## Slide 4: Which elements constitute the source in SRW?
Electron beam (SRWLPartBeam):
storage ring current and energy
single electron initial condition ( and – first order statistical moments).
electron beam second order moments (Twiss parameters or RMS values).
Magnetic field container (SRWLMagFldC):
magnetic field structure:
  arbitrary 3D field (SRWLMagFld3D)
  dipole magnet (SRWLMagFldM)
  undulator (SRWLMagFldU)
center positions of magnetic field elements ()
Stokes container (SRWLStokes or SRWLWfr):
allocates arrays for electric field calculations.

## Slide 5: How is it done?
Spontaneous emission by a relativistic electron in free space (retarded potentials approach in Gaussian CGS):
where is a particular electron trajectory, is the relative velocity of the electron; , , ; denotes the observation point.
The phase in the exponent can be expanded assuming small observation angles while still preserving the variation of with the electron position (near field calculation):
with as integration variable.
Chubar, Review of Scientific Instruments 66(2), 1872–1874 (1995)
Chubar, Infrared Physics & Technology 49(1–2), 96–103 (2006)

## Slide 6: How is it done?
Spontaneous emission by a relativistic electron in free space (retarded potentials approach in Gaussian CGS):
where is a particular electron trajectory, is the relative velocity of the electron; , , ; denotes the observation point.
Asymptotic expansion of the radiation integral (to accelerate computation):
Chubar, Review of Scientific Instruments 66(2), 1872–1874 (1995)
Chubar, Infrared Physics & Technology 49(1–2), 96–103 (2006)

## Slide 7: How is it done?
Spontaneous emission by whole relativistic electron beam in free :
The incoherent synchrotron radiation is given by:
And the coherent synchrotron radiation is given by:
The particle density distribution in the 6D phase space is described by the function and normalised to 1:
Chubar, Review of Scientific Instruments 66(2), 1872–1874 (1995)
Chubar, Infrared Physics & Technology 49(1–2), 96–103 (2006)

## Slide 8: Examples
Live demo using OASYS…

## Slide 9: Thank you!