## Slide 1
Introduction to XOPPY
Basics X-ray Optics calculations
Manuel Sanchez del Rio
srio@esrf.eu
Advanced Analysis & Precision Unit, MEG/ISDD, ESRF
XOPPY

## Slide 2: Transport of power in a Beamline
Outline:
Intro
Basics concepts
XOPPY History
Optical elements: characteristics and absorbed power.
Flux that arrive to the sample
XOPPY

## Slide 3: Hyerarchical simulations with Oasys
Analytical model (by hand and XOPPY)
Ray tracing (Shadow4)
Hybrid model (Shadow44)
Wave optics (WOFRY) 1D Coherent Mode Decomposition
Mode Decomposition (2D CMD also possible)
Monte Carlo (multi e-) wave optics (SRW)
Ref. M. Sanchez del Rio et al, JSR 26 1887 (2019)
https://doi.org/10.1107/S160057751901213X
COMPLEXITY

## Slide 4: Basics concepts (hand calculations)

## Slide 5: The Beam: Spectrum and Size
Size: FWHM
If profile is Gaussian
FWHM = 2.355
x
y
A light beam or beam of light is a directional projection of light energy radiating from a light source.
Collection of particles [photons]
Collection of waves
The main parameters can be represented:
As histograms if they are discrete variables
As functions if they are continuous variables
Spectrum I(E) Beam profile I(x,y) [cartesian]
I(E,x,y)
CORRELATED!

## Slide 6: Estimate Flux and size (H, V) from the source
Flux: Photons per second per (variable) bandwidth (0.1% E)
Source: 2.9 1014 photons/s/ (0.001 bandwidth)
ML monochromator DE/E=0.01, therefore:
2.9 1015 photons/s (integrated)
71 x 10 um^2 (H x V)
16 x 12 urad^2 (H x V)

## Slide 7: How does the beam propagates in free space?
If rays: Need direction or angle and propagates as a straight line (without changing the intensity)
If waves we need an integral propagator: Fresnel etc. (changing the intensity distribution, conserving the integrated intensity
?
z1
If we know how to propagate, we can define Brightness or Brilliance:
peak intensity, on-axis, and far away
[photons/s/0.1%bw/mm^2/mrad^2]
z2

## Slide 8
How the beam propagates through components – Optical Elements
Crop (slits) Focus (change propagation) Attenuate/Reflect
Redefine size change the direction change the intensity
IDEAL SLIT IDEAL LENS ATTENUATOR / MIRROR
material & density
thickness
X-ray beam
f
Beer-Lambert Law

## Slide 9: Transfer Matrix: the simplest ray-tracing
“linear” black box
Straight propagation: distance x divergence [not quadratic!]
[same divergence]
Lens: : [no-propagation]
[direction changes with x]
Mirror: (normal incidence) [grazing incidence, Coddington equations]

## Slide 10: Transfer Matrix: typical p:q focusing
= =
M [magnification]
[1/M + a linear term with x0]
p
q
S
s = S x M
Lens equation Magnification

## Slide 11: Other matrix-based systems: The electron beam dynamics
General
No z-coupling
Finite alpha
Symmetry point
Statistically distributed bunches
P1
P2
P3

## Slide 12: Extending Transfer Matrix: Phase Space Analysis, Ray tracing
Phase Space Analysis:
https://doi.org/10.1364/AO.47.00E116
Too basic:
Gaussian-shaped beam at the source
Gaussian elements
Linear (matrix) operators.
These limitations are not in full ray tracing [shadow]:
18D phase space
fully non-linear operators (able to calculate aberrations, surface errors, tolerances, etc.)
…

## Slide 13: Hand-calculations. Example ESRF ID16A Beam sizes and flux
Flux: use geometrical crop
  Initial (source): 2.9e14 / 17 ph/s/eV
  Monochromator: x 1e-2 * 17000 = 170
  Crop VSS (none for EBS)
  KBV (60mm) 7.1%
  KBH (26mm) 40%
  Total 2.85%. Thus 8.3 1013
Apply mirror reflectivity

## Slide 14: XOPPY history
XOP (X-ray Oriented Programs) (http://dx.doi.org/10.1063/1.1147376)
          a user interface to useful tools for the beamline designer
                collaboration ESRF-APS (M. Sanchez del Rio and Roger J. Dejus)
                it included some tools for synchrotron spectra (US, URGENT), and a bunch of pieces of SHADOW to compute BM and wiggler sources, crystal, multilayer and mirror reflectivities.
                The interface was written in the IDL binding Fortran codes
XOP evolved (2004-2011) with mode dedicated codes and a new optical constants database (DABAX) (http://dx.doi.org/10.1117/12.893911 )
The XOP concept migrated to OASYS, and new interfaces were created in python (therefore the name of the add-on XOPPY) but always maintained the initial philosophy of “toolbox”
OASYS-XOPPY uses xraylib. Many new features have been added: 3D calculations (E,x,y) SRCalc Scripting DABAX available
1996
2004
2009
2013-2025

## Slide 15: Simulation of source emission
XOPPY
Source spectrum (Photon flux or power vs Energy)
bending magnet
Wiggler
Bending
magnet
Undulator

## Slide 16: Undulator emission simulation
XOPPY
U42
Slit
30 m

## Slide 17: Undulator emission simulation
XOPPY
U42
Slit
30 m
~50 eV
1st harmonic

## Slide 18: Undulator emission simulation
XOPPY
U42

## Slide 19: Undulator emission simulation
XOPPY
U42

## Slide 20: Undulator emission simulation (gap)
Gap
For ID21 U42b:
a=1.9395
b=1.0164

## Slide 21: Undulator emission simulation
Gap
Reducing
the gap
incrementing K
larger wavelength
(lower energy)

## Slide 22: Undulator emission simulation
Gap
Reducing
the gap
More power
Central cone flux
On-axis flux
Ref:

## Slide 23: Simulation of source emission
Undulator power density (power vs x, y)
Undulator spectral flux density (flux/power vs x, y, E)
Wiggler spectral flux density (flux/power vs x, y, E)

## Slide 24: Simulation of source emission
Undulator spectral flux density
(flux/power vs x, y, E)
Wiggler spectral flux density
(flux/power vs x, y, E)
y
E
Photon flux
Photon Energy [eV]
1000 5000 10000 15000 20000
x

## Slide 25: Power transport on a beamline
Optical components that could be present in a beamline:
Source
Front end
Water-cooled
slits
Windows
Primary slits
Primary mirrors
Monochromator
Focusing system
Sample
KB mirrors

## Slide 26: Undulator power density (Power vs x, y)
For example, this tool is very useful to get the heat load on a slit:
undulator
Water cooled beamline slit

## Slide 27: Undulator power density (Power vs x, y)
In most of the beamlines at the ESRF the are horizontal slits at 16 m from the source:
X-ray beam
Project over the slit surface (2o angle)
Perpendicular to the beam
Finite element analysis

## Slide 28: Power transport on a beamline
Optical components that could be present in a beamline:
Slit 1
Projected size at
downstream element (A)
Distance from the source (d)
Aperture (a)
Distance from the source (D)
Source
Source
Front end
Water-cooled
slits
Windows
Primary slits
Primary mirrors
Monochromator
Focusing system
Sample
KB mirrors

## Slide 29: Filter (window) absorption
Filters of different thickness
Filters of different materials

## Slide 30: Power absorbed by a filter
Heat load on filters @ 23 m with a projection of 2 mm x 1 mm:
U42-EBS
Material | Thickness [mm] | Absorbed Power [W]
Be | 300 | 19
Diamond | 300 | 40
thickness
material & density
X-ray beam

## Slide 31: Power absorbed by a filter
Heat load on filters @ 23 m with a projection of 2 mm x 1 mm:
Be (300 mm)
Diamond (300 mm)

## Slide 32: Power transport on a beamline
Optical components that could be present in a beamline:
Slit 1
Aperture (a)
Source
Absorption by filters
Absorption power by mirror
Source
Front end
Water-cooled
slits
Windows
Primary slits
Primary mirrors
Monochromator
Focusing system
Sample
KB mirrors

## Slide 33: Mirror absorption
Same material, different angles
Same angle, different coatings
Reflectivity
Reflectivity

## Slide 34: Mirror absorption
1st Harmonic
3rd Harmonic
1st Harmonic
3rd Harmonic
Example of reflection, primarily mirrors @ 30 m
Absorbed power 113 W
Absorbed power 52 W

## Slide 35: Power absorbed by a mirror
Heat load on mirrors @ 30 m:
Si (7 mrad)
Diamond (100 mm) + Rh (3 mrad)

## Slide 36: Other optical elements in XOPPY
Multilayers
[W(2.5)/Si(2.5)]50
1.4o

## Slide 37: Other optical elements in XOPPY
Crystals
Si (111)
22 keV
Rocking curve
Bragg or reflection
Double crystal monochromator

## Slide 38: Calculation of flux at the sample position
Exercise: estimate the photon flux at the sample position.
KB slits
51 m
Source
Primary mirrors
Monochromator
Focusing system
Sample
KB mirrors
Ni coated
6 mrad
Slits aperture 1 mm x 1 mm
Ni coated 7 mrad
Si (111)
ESRF-ID21
5 keV

## Slide 39: Calculation of flux at the sample position
Exercise: estimate the photon flux at the sample position.
KB slits
51 m
Source
Primary mirrors
Monochromator
Focusing system
Sample
KB mirrors
Ni coated
6 mrad
Slits aperture 1 mm x 1 mm
Ni coated 7 mrad
Si (111)
ESRF-ID21
5 keV